## Slide 1: Module 3: Dealing with Files
Robotics – ll

## Slide 2: Objectives
Understand the file access block and its configuration
Create and use files inside NXT programs

## Slide 3: Introduction
Your computer uses files to store music, pictures, programs, documents, and other kinds of information.
The NXT also uses files to store various types of information, such as your programs, images used by the display block, and the sounds used by the sound block.
Types of Info stored in the NXT:

## Slide 4: Files in NXT-G programs can be used to:
Store data collected by the program as it runs. For example, storing high scores for a game, or a map generated by a maze-solving robot.
Store program settings such as the speed the robot should use or trigger values for sensors.
Collect sensor data as part of an experiment or a test program. For example, collecting weather information from sensors.
In this module, you will learn how to create and use files in NXT programs

## Slide 5: File Access Block
The File Access block allows you to create your own files on the NXT.
Such files can be used to store any data that your programs use. For Example, you can store the values of the sensors to analyze and process them.
File Access block can be found in the Advanced group on the Complete Palette.
Action
File Type

## Slide 6: File Access Block
The File Access block can be configured using either the Configuration Panel OR data wires.

## Slide 7
To use the File Access block, you must set the following parameters:
1. Action
2. File Name
3. File Type
How to use the File Access Block
Action
File Type

## Slide 8: 1. Action The Action setting tells the block what you want to do with the file.
You can do the following four operations:
1. Write: Stores information in a file. If the file doesn’t exist, the access block will create one; otherwise, the new data is added on at the end of the existing file.
2. Read: Retrieves information from a file. The value read from the file is passed to other blocks in the program using a data wire (Text or Number data wire)
3. Delete: Deletes a file. You delete a file if you want to replace the information in it. For example, if you want to set the high score of a game, you need first to delete the file and then write the new value.
4. Close: Closes the file. You need to close the file before you can read from, write to or delete it.

## Slide 9: 2. File Name: The file name setting sets the name of your file.
The name of the file cannot exceed 15 characters.
It can include numbers, letters, spaces, and most of the special characters such as * and #.
When naming a file, use meaningful filenames that reflect the actual content of your files.
To create a new file, enter the file name in the name box.
To reuse an existing file, select it from the file list and the name box will be filled automatically.

## Slide 10: 3. File Type: The file type setting tells the block which data type you are using.
The file access block can read and write both numbers and text values.
When the action is set to Write, the value can be supplied via a data wire or the Configuration Panel. With Text selected for Type, you can enter the text to write to the file in the Text box. When writing a number, you can enter the number to write to the file in the Number box.
When the Action is set to Read, the data will be available on either the Text out or Number out data plug, depending on the Type setting

## Slide 11: Lab Activities 1&2 (pages 7 – 11) Review Exercise (pages 12 – 13)